## Slide 1
Low Cost Real-time Room
Occupancy Indicating System
Chirag Shah, Srijal Poojari Guide: Prof. Priya Deshpande
Department of Electronics Engineering, Sardar Patel Institute of Technology, Andheri (West), Mumbai-400058
Introduction
A corporate office of 400 employees: 250 employees on 7th floor, 150 employees on 3rd floor
7th floor has 10 meeting rooms and 3rd floor has 5 meeting rooms
Anyone can book any meeting room for any time (if the room is available) using a mobile app
This is an open office – hence if anyone wants to have a discussion then they need to go to a meeting room
Meeting rooms are always in demand
Solution Design
Highlights
Conclusions
References
Authors Contact Details
[1] Sparkfun.com, “nRF24L01+ Transceiver Hookup Guide”, [Online]. Available:https://learn.sparkfun.com/tutorials/nrf24l01-transceiver-hookup-guide [Accessed: 10-Feb-2018]
[2] geekstips.com, “Internet of Things Project – Communication between ESP8266 modules”, [Online]. Available: https://www.geekstips.com/two-esp8266-communication-talk-each-other/ [Accessed: 10-Feb-2018]
[3] Scargill, “Networking the nef24l01”, [Online]. Available:https://scargill.wordpress.com/2013/05/17/networking-the-nrf24l01/ [Accessed: 10-Feb-2018]
We may have an opportunity to implement this in real life within the corporate environment
Bhartiya Vidya Bhavan’s, Sardar Patel Institute of Technology, Electronics Engineering Department, Andheri (W), Mumbai-400058.
chirag.shah@spit.ac.in,+91769168825 (M)
srijal.poojari@spit.ac.in, +91
Problem Definition
If someone wants to have a meeting spontaneously without booking the room then the he/she will have to go from room to room to check the occupancy status of the room
Someone may book the room but if the meeting is cancelled then he/she may not cancel the booking, this may stop others form using it during that time since there is no way to check the occupancy status without actually going to the room
We used a PIR sensor to detect occupancy of the room
The sensor is connected to an Atmel microcontroller which relays the information to a central device via radio modules configured in a mesh configuration
The central device will push the data to the internet using a WiFi module
All the devices are battery powered
We create a complete end-to-end product including getting PCBs manufactured for the devices and designing the web interface
We will create a real-time wireless conference room occupancy monitoring system
Each room will have one or more devices which will detect the occupancy of the room
This data will be uploaded to a central server/device over which will keep track of the occupancy of all the rooms
The occupancy of each room can be viewed on a web interface
This data can be integrated with the existing mobile app(this is outside the scope of this project)
Results
We created a complete end-to-end product
Got the PCBs manufactured for the devices
3D printed the product box
Designed the web interface
Created a real time wi-fi mesh
Here are a few photos of the end product
Highlights
We created a complete end-to-end product
Got the PCBs manufactured for the devices
3D printed the product box
Designed the web interface
Created a real time wi-fi mesh